Deer Feeder Status Requirements:

# Introduction
The goal of the project is to create a sensor / microprocessor / cellular modem combination that will measure the quantity of corn available in a Deer Feeder and send the daily status result, using the cellular network. The system should also identify when the Deer Feeder is empty. The sensor package should be installed on the Deer Feeder and be powered by the feeder power system and utilize the existing solar panel for recharging.

# Basic Design Components:
1) Distance Sensor – HC SR104 ultrasonic distance sensor, 5v
2) Hologram Dash/DashPro Cellular connection kit
3) Hologram Cloud Data respository
4) 12 v feeder battery system
5) 20 v solar panel

# Minimally Viable Product (MVP):
## Feeder Gauge
Measure the distance from the deer feeder lid to the surface of the corn. Maximum distance will be when the feeder is empty.
## Take Measurement
Every 24 hours, take 5 measurements and average the result
## Send Measurement to Cloud
Once the measurement has been successfully taken, wake up the cellular modem, make a connection and send result to the cloud.
## Recharge Battery
Use the existing solar panel to recharge the built in battery.
# Additional Requirements:
## Feeder Action / Health
Record the time and duration of the feeder action. Send the resulting data when the daily message is sent
## Empty Notification
Send an SMS notification when the feeder is empty.
# Software Design
Use Arduino IDE, compiled code.
## Distance Measurement
Modify the NewPing code to compile on the Arduino with the Hologram Dash card
Separate module (function) to take the measurement. Use the built in average function to average over 5 readings.
- call function feedDistance = MeasureFeed();
- return distance in cm
## Send Data to Cloud
Use the CloudBegin to initialize the connection to the cloud. Send the data, loop to monitor success. If not success after 5 minutes, set exception and retry.

# Next Steps
## Hardware
1. Power up and test Dash Pro. Just get back to where I was before
2. register the Dash Sim 2
3. register Dash Sim 3
4. Power up and test Dash Sim 2
5. Power up and test Dash Sim 3
6. Configure and label Dash 1 for Battery (remember the jumper)
7. Design and configure project box
8. Locate external antenna
9. Design and integrate Sun Buddy solar panel charging
## Software
1. Register Sim 1 and Sim 2 on account
2. Provision account with sufficient funding
3. Update Arduino package
4. Update firmware for Dash 1 & 2
# Hardware Information
## Dash Pro 1
1. Konekt Kon -LU200 2015-11-17
  1. Ublox Modem, Model – LISA-U200 820100.0312.000
  2. IMEI 358683063825229
  3. SIM 8944501006151414846
## Dash (1)
1. Hologram Dash Rev 2 2016-07-17
  1. Ublox Modem, Model – SARA-U260 830000.0412.000
  2. IMEI 353162076254433
  3. SIM 8944501006151395359
## Dash (2)
1. Hologram Dash Rev 2 2016-07-17
  1. Ublox Modem, Model – SARA-U260 830000.0404.000
  2. IMEI 353162071237664
  3. SIM 8944500803165573562
# Power Wiring Design

Feeder
Timer
Solar
Panel
Feeder
Battery
Solar
Charger
Dash
Battery
Dash
20 volts
12 volts
12 volts
3.7 volts
3.7 volts

# Electronics Wiring Design
BreakOut Board	Dash	DHT	US-100	Ethernet	4-Wire
Power	13	3.3V		Orange	Red
L15	L4 (D10)	Data		Orange/W	White
GND		GND		Green/W	Grey
Power			3.3V Pin 1	Blue	Red
L11	L8 (D14)		TX Pin 2	Brown	Black
L13	L6(D12)		RX Pin 3	Brown/W	White
GND			GND Pin 4	Blue/W	Grey
GND (L17)	L02(GND) (jumper
Power (R7)	R12 (3.3v) (jumper)